## Slide 1: Honeywell PM8088 performance tuning
May 23rd 2014
Proprietary and Confidential – Disclosed under NDA

## Slide 2: Agenda
Application Tuning Objective
FP/timestamp enhancement example –RTPReceptionStats::noteIncomingPacket
Tuning Result

## Slide 3: Application Tuning Objective
Observation refresh
  strace shows the gettimeofday syscall very frequently, 2 times over the recvmsg syscall, which means 2 gettimeofday syscall of each packet received. The time expended in gettimeofday is close to that of recvmsg.
  oprofile shows 33% of the total CPU time is on fpu_emulator_cop1Handler. Honeywell confirms the application dynamic library involves float point calculation in RTP timestamp processing.
Tuning Objective
  Enhance the local time (gettimeofday) efficiency
  Replace the float point with integer ones.

## Slide 4: FP/timestamp enhancement example – RTPReceptionStats::noteIncomingPacket
code snippet for tuning in RTPReceptionStatus::noteIncomingPacket
  Record the inter-packet delay
    get and calculate the current time stamp base on the timeval returned by gettimeofday()
    gettimeofday() – syscall and timeval struct overhead
    inter-packet us gap
    timeval struct based – tv_sec/tv_usec to us conversion overhead
  Jitter computing
    Float point calculation
    Timeval struct based – tv_sec/tv_usec to timestamp conversion overhead
  Presentation time computing
    The RTP timestamp diff added to the last sync timeval struct for presentation timeval struct
    timeval struct to timestamp conversion and float point processing overhead

## Slide 5: FP/timestamp enhancement example – RTPReceptionStats::noteIncomingPacket
PMC tuning in RTPReceptionStatus::noteIncomingPacket
  Replace all timeval struct with local timestamp read from CPU counter, fill in the presentation timeval struct in the end of the function
  All float/double variables to int_32/int_64 variables
  Replace mul/div operation with shift operation wherever possible

## Slide 6: Tuning result test configuration
Test setup/method
  Media server: VLC on host server
  Media client: Live555 testRTSP application on pm8088 eval board
  Two processes of Live555 client instance are running simultaneously on the pm8088 eval board, one for optimized, the other for un-optimized. Two processes run on separate CPUs.
  The server duplicates the same load to the two Live555 clients.
  Log the CPU utilization for both processes and compare the difference.

## Slide 7: Turning result test result
Test result
  Single live555 client: 8 streams, total 56Mbit/s throughput
  Un-optimized live555 client CPU utilization
    CPU util: usr 10.4%, sys 60.2%, total 70.6%
    fpu_emulator_cop1Handler: 10.2813%
    gettimeofday/recvfrom: 4.62
  Optimized live555 client
    CPU util: usr 10.3%, sys 38.4%, total 48.7%
    fpu_emulator_cop1Handler: 2.4790%
    gettimeofday/recvfrom: 2.54
  Performance improvement
    CPU utilization dropped 31%
    FP handling dropped 75.9%
    gettimeofday call dropped 45%

## Slide 8: Turning result test result analysis
Analysis
  CPU system time has been dropped a lot, due to gettimeofday/FPU optimization
  The live555 client PMC is testing with calls select instead of epoll. If switching to epoll, which is much more efficient than select, the overall performance enhancement ratio could be bigger than 31%.
  There’s remaining gettimeofday/FP handling, could be further optimized out for more performance enhancement

## Slide 9: Tuning result performance projection
Honeywell test result on 15th May
Projection
  In test1, PMC platform opt brought the receive cpu utilzation drop to ~35% under target loading level.
  In the test2/3 didn’t bring in any performance improvement. According to PMC application tuning test result, we expect roughly 30% more CPU drop if taking in PMC application optimization recommendations.
 | PMC platform opt | Gettimeofday opt | FP opt | CPU total % | CPU 0 % | CPU 1 % | CPU 2 % | CPU 3 % | fpu emu % | libc02.11.3.so %
Test1 | x |  |  | 34.825 | 25 | 51.9 | 52.9 | 9.5 | 32.7064 | 5.1004
Test2 | x | x |  | 36.525 | 24.5 | 59.8 | 55.9 | 5.9 | 32.8848 | 5.2167
Test3 | x | x | x | 31.6 | N/A | N/A | N/A | N/A | 7.4548 | 36.3981