## Slide 1: Honeywell PM8088 performance tuning
Jun 6, 2014
Proprietary and Confidential – Disclosed under NDA

## Slide 2: Content
Observation
Suggest to Honeywell
Update from PMC

## Slide 3: Observation
Summary
  Even CPU power remains ~100% idle for current 30 forward streams, but more CPU power will be required when enabling 128 forward streams
    The 128 forward streams might consume ~200% CPU, since 30 forward streams consume about 50% CPU
  Points
    The forward flow consumes heavier than receive flow
      The 128 receive streams brings about 130% usage to StreamServer and 32.5MBps to network
        Equals to 1.016% CPU usage per receive stream
      The 30 forward streams brings about 50% usage to StreamServer and 7.8MBps to network
        Equals to 1.67% CPU usage per forward stream
    The forward flow uses just two UDP socket
      Totally 256 UDP socket been used without forward streams
      Totally 258 UDP socket been used with forward streams
    CPU exhausting is not found in the log
      The CPU usage is mostly healthy with the 30 ways forward flow
CPU | %usr | %sys | %iowait | %soft | %idle
all | 38.53 | 20.23 | 1.13 | 14.43 | 25.68
0 | 4.13 | 5.41 | 0.33 | 48.91 | 41.22
1 | 52.06 | 27.72 | 0 | 2.1 | 18.12
2 | 52.61 | 27.11 | 0.07 | 2.48 | 17.74
3 | 45.39 | 20.72 | 4.1 | 4.17 | 25.61

## Slide 4: Suggest to Honeywell
Pending questions
  How to find the “packet loss” in the evaluation platform with forward stream, does it happen during the logging period (the log sent on 2014-06-04)?
  What’s the level of forward flow, is it a “UDP packet level forward” or “RTP/RTCP protocol transformed level forward”?
Suggested action for further analyze
  Get a log which can see the mentioned “CPU decrease to 10% or lower”
    Use the updated v04 script, which calculates the Ethernet statics
  Test with CPU overclock to 1.1GHz to see how much it helps in the full application loading
    PMC will provide a firmware update to enable the CPU 1.1GHz

## Slide 5: Update from PMC
Completed
  Modifications
    The epoll modification
    The removal for gettimeofday(), which is related to epoll delta time calculation (in the SingleStep())
  Result
    CPU utilize for RTP receiving decreased ~52%, by comparing to first patch
    CPU utilize for RTP receiving decreased ~69%, by comparing to original code
Ongoing
  The scheduler optimization according to Honeywell’s analyze
    Under estimation
 | %CPU, 16 recv
orig | 36
patch01 | 23
patch02 | 11