## Slide 1: Honeywell PM8088 performance tuning
Jul 4, 2014
Proprietary and Confidential – Disclosed under NDA

## Slide 2: Content
Observation
Next step

## Slide 3: Observation
Summary
  The CPU usage decreased much after thread number/assignment change

## Slide 4: Observation
  system-log
  CPU usage decreased about 43.5%(absolute value of the 400%)
    Looks very good since the estimated CPU usage would be 266% for 128 streams
  Interrupt number also decreased about 30%
    System is working more efficiency
  The UDP/NIC packet number are mostly the same for both input and output
    This means the two tests having same stress on streams
 | rcv | save | fwd | rcv0 | rcv1 | save | softirq | fwd0 | fwd1 | fwd2 | fwd3 | sum | int/s-all | int/s-net | rx-n | rx-KB/s | tx-n | tx-KB/s | udp-in-n | udp-out-n
avg a+v | 64 | 64 | 64 | 31.6 | 30.9 | 19.3 | 28.8 | 17.3 | 16 | 16.8 | 15.8 | 176.5 | 12853 | 4204 | 11176 | 14836 | 10829 | 14458 | 11041 | 10657
avg a+v thread reassign | 64 | 64 | 64 | 24.9 | 25.6 | 16.9 | 25.6 | 40 | 0 | 0 | 0 | 133 | 8962 | 4300 | 11216 | 14883 | 11292 | 14883 | 11079 | 11118

## Slide 5: Observation
  oprofile-log
    The memcpy call sample decreased about 35.2% (from 9910 to 6422)
      Not very expected, since stress are mostly the same between the two test streams
 |  | a+v r64s64f64 |  | a+v r64s64f64 thread Adj. | 
app_name | symbol_name | samples | % | samples | %
vmlinux | r4k_wait_irqoff | 63868 | 39.4174 | 75968 | 46.5504
vmlinux | __pastwait | 20916 | 12.9087 | 28308 | 17.3461
libc-2.11.3.so | memcpy | 9910 | 6.1162 | 6422 | 3.9352
vmlinux | __copy_user | 5130 | 3.1661 | 4882 | 2.9915
vmlinux | _raw_spin_unlock_irqrestore | 3562 | 2.1984 | 2095 | 1.2837
vmlinux | finish_task_switch | 2602 | 1.6059 | 1430 | 0.8763
vmlinux | mips_sc_inv | 2181 | 1.346 | 2046 | 1.2537
vmlinux | r4k_dma_cache_inv | 2106 | 1.2998 | 1908 | 1.1692
libc-2.11.3.so | _wordcopy_fwd_dest_aligned | 1674 | 1.0331 | 1305 | 0.7997
vmlinux | __do_softirq | 1672 | 1.0319 | 1499 | 0.9185
vmlinux | r4k_blast_dcache_page_dc32 | 1050 | 0.648 | 723 | 0.443
libc-2.11.3.so | vfprintf | 931 | 0.5746 | 665 | 0.4075
vmlinux | bnx2_poll_work | 816 | 0.5036 | 709 | 0.4344
libpthread-2.11.3.so | pthread_mutex_lock | 795 | 0.4906 | 581 | 0.356
libc-2.11.3.so | memset | 713 | 0.44 |  | 
StreamingServer | RTPStream::Write() | 706 | 0.4357 | 478 | 0.2929
libpthread-2.11.3.so | __pthread_mutex_unlock_usercnt | 579 | 0.3573 | 470 | 0.288
vmlinux | ring_buffer_consume | 545 | 0.3364 | 486 | 0.2978
CPSModule | find_fit | 528 | 0.3259 | 816 | 0.5
vmlinux | bnx2_start_xmit | 514 | 0.3172 | 475 | 0.2911

## Slide 6: Next step
Follow up on audio enabled stream flow